Form 1.1 Installation checklist: System evaluation.

A. Contact information

Client name: _____________________________________	 Reference #: ___________________________

Permits #:

Site address/county:

Mailing address: ___________________________________________________________________________

Home Phone: 	 Cell phone: 	 Email:

Designer/Planner: 		 License #:

Phone #: 	 Cell phone: 	 E-mail:

Site Evaluator: 			 License #:

Phone #: 	 Cell phone: 	 E-mail:

Installer: 	 		 License #:

Phone #: 	 Cell phone: 	 E-mail:

O&M Service Provider: 		 License #:

Phone #: 	 Cell phone: 	 E-mail:

Inspector(s): 		 License #:

Phone #: 	 Cell phone: 	 E-mail:

B. 	Job Contracting

I.  	Design review (information collected obtained from design)

1. 	Plan provided       			( Yes  (  No

( Approved  		(  Draft	(  Includes special considerations

( New construction 	( 	 Repair

2. 	Plan complete       			( Yes  (  No

( All components specified  	(  Component size specified

( Component location specified  	(  Accessibility for maintenance specified

(  Components readily available

3.	 Soil and site evaluation report provided       		( Yes  (  No

4. 	Hydraulic loading specified       			( Yes  (  No

Design flow: __________________ Gal. per day

Peak flow: ____________________

5. 	Organic loading specified       			( Yes  (  No

(  Residential (assumed)	( Commercial (assumed)

(  Specification: 	 (mg/L or lbs. BOD/TSS/FOG per day)

6. 	Tank buoyancy calculation provided       		( Yes  (  No

7. 	Treatment train components (Check all that apply):

Tanks:

( Septic/Trash/Processing (tank): 		 ( Pump: Timed dosed system:

( Pump: Demand dosed system: 		 ( Holding tank:

( Dosing tank(s): 		 ( Other:

Advanced treatment components:

( Disinfection unit: 		 ( Aerobic treatment unit:

( Constructed wetland: 		 ( Media filter:

( Other:

Final treatment and dispersal components:

( Trench/Bed – gravity:	 ( Drip field:

( Evapotranspiration bed:

( Trench/Bed – Low pressure distribution: 	 ( Spray field:

( Mound system:

( Bottomless media filter:	 ( Other:

II.  	Site review

1. 	Site planning materials match/describe site 			( Yes 	(  No

2. 	Planning materials describe a constructible treatment train 	( Yes 	(  No

( Treatment train components available

( Plumbing stub-out elevation 		( Existing 			( From design _________

3. 	Owner interviewed during site/plan review 		( Yes	(  No

4. 	Site requires special construction considerations 	( Yes	(  No

III.  Bidding & contracting

1. 	Bid development       				( Yes 	(  No

( Cost estimation	( Special equipment & installation considerations

2. 	Bid submitted (date):		________________

3. 	Bid accepted (date):       	________________

4. 	Contract submitted (date):	________________

( Standard items	( Exclusions	( Change orders	( Payment schedule

5. 	Contract accepted (date):		________________

C. 	System planning & installation

1. 	Construction scheduling completed (date): 		________________

2. 	Preconstruction site visit (date):		 	________________

3. 	Installation started (date):			________________

4. 	Complete installation checklists

( Pretreatment components                                  		( Yes	(  No

( Dosing system and controls				(NA	( Yes	(  No

( Final treatment and dispersal component		( Yes	(  No

5. 	Complete startup checklists

( Pretreatment components                                  			( Yes	(  No

( Dosing system and controls				(NA	( Yes	(  No

( Final treatment and dispersal component		( Yes	(  No

6. 	Intermediate inspections 				(NA

( Type: 	 Name: 	 Date: 	 Time:

( Type: 	 Name: 	 Date: 	 Time: 				( Type: 	 Name: 	 Date: 	 Time:

7. 	Final regulatory installation inspection 		 Date: 		 Time:

8. 	Information provided to owner

( Final plans/As-built drawings	( Service policies/Warranties

( Operation and maintenance guidance	( Monitoring requirements/guidance

( Educational resources                                 	( Authorization to operate wastewater treatment system

( Service provider contracts

9. 	Overall final system condition

( Installation complete	( Landscaping needed

( Installation incomplete	( Startup needed

This report indicates the condition of the above wastewater treatment system at the time of the installation inspection.

Final survey completed by: 			 Date:

# Text boxes

Comments:

Comments: