Form 11.2. Startup checklist:  STA

Client name: 	 Reference #:

Permit(s) #:

Completed by: 	 Time: 	 Date:

1. 	Type

a.	Method of application to soil: (attach appropriate checklist)

( Gravity distribution	( Pressure-dosed gravity

( Pressure distribution   	( Siphon to gravity

b.	Method for treatment in the field:

i. Below-grade

( Shallow, narrow pressurized trench (LPP)

( Low-pressure distribution (LPD)  		( Bed

( Parallel trench    	( Serial trench	 	( Sequential trench

ii. Above-grade

( Mound         	( Modified mound     	( Areal fill

( At-grade           	( Bottomless media filter

2.	Fill/media

a.	Fill type:

b.  	Media type

( Chamber

Manufacturer:

Model:

( Polystyrene aggregate

Manufacturer:

Model:

( Sand	( Washed rock

( Other, Type:			    Source:

c.   	Inspection ports   							( NA

i. 	Access

(  To grade   	(  Above-grade 		in.   (  Below-grade		in.

ii. 	Secured      								(

3. 	Effluent distribution:

a.	Distribution method:  ( Gravity distribution     ( Pressure distribution

b.	Gravity distribution device					( NA

i.	Type:

(  Distribution box    	( Drop box

(  Header    	Description of header:

Other:

ii.	Access:

(  None		( Riser

(  Other:

c.	Pressure manifold							( NA

i.	Manifold feed configuration

(  End      ( Top     ( Bottom      ( Center     ( Dual center     ( Looped

ii. 	Access/protection

(  Installed in valve box to grade

(  Installed in valve box 					in. below-grade

(  Cleanout installed	(  Separate pressure port installed

iii. 	(  Distal head checked, 					ft

d.	Valving    							( NA

i.	Type

( 	Alternating valve, Type:				ft

(	Zone or sequencing 	 ( Globe       	( Gate

(	Ball 			 ( Other

ii. 	Access/protection

- In dosing tank

(  	Valve box to grade

(  	Valve box 						in. below-grade

(     Cleanout installed

iii. 	Confirmed operable     				(

e.	Laterals 							( NA

(     Installed on contour

(     Level or sloped according to local regulations

(     Cleanout installed				( NA

Access

(     Valve box to grade

(     Valve box 						in. below-grade

f. 	Orifices in laterals (pressure distribution)							( NA

i. 	Operating pressure verified	 			( NA 	( Yes

Location:

Measured at:  								ft

4.	Final cover and landscaping

a.   	Depth of cover					in.

b.   	Type of soil cover                                   		( NA	( Yes  	( No

c.   	Surface sloped to shed rainwater		(

d.	Surrounding landscape graded to prevent stormwater runon		(

e.	Vegetation covering site/planted		(

f.   	Evidence of negative site impacts due to construction methods 	( Yes 	( No

# Text boxes

Comments:

Comments: