Form 8.2. Installation checklist: Tanks			Form 		 of

Note: A separate checklist should be included for each tank installed.

Client name: 			 Reference #:

Permit(s) #:

Completed by: 		 Time: 					 Date:

1.	Tank description

a.	Type of tank:

( Septic tank   	( Trash tank   	( Grease trap    	( Processing tank

( Holding tank  	( Pump tank    	( Siphon tank

( Surge/Flow equalization tank   	( Recirculation tank

b. 	Manufacturer:

Model #:

c.  	Material:

( Concrete       ( Fiberglass       ( Plastic/Poly

( Other:

d.    Manufacturer’s load-bearing rating: 	 (psf or maximum burial depth)

e.	Tank dimensions and capacities:

Exterior dimensions: 	 	Interior dimensions:

Exterior height of inlet invert:

Exterior height of outlet invert:

Effective depth:  	in.	Total tank capacity: 			 gal

Gallons per inch (gpi):  	gal/in.

Compartmented:  		( NA	( Yes 	( No

Capacities of compartments:  1)	    gal	2) 	            gal

If compartmented dosing tank, wall rated:	( NA	( Yes 	( No

Multiple tanks:		( NA	( Yes 	( No

Capacities of multiple tanks:  1)	    gal	2) 	            gal

f.	Tank seam

Location: 	( NA	   (  Mid      (  Top

Sections joined:

( Pre-delivery by supplier	( Onsite by supplier	( Onsite by installer

Tank sealant(s) used:

(  Butyl mastic	( Butyl tapes wrap	( Two-part epoxy

( Two-part epoxy and stainless fasteners    	(  Other:

g.    ( Tank structural integrity verified prior to setting

2.	Excavation/ Setting tank

a.	Stake location of tank(s)			(

b.	Verify required inlet/outlet elevations 			(

c.    Water present in excavation		( Yes  	( No

(  If yes, dewatering performed during construction

- Bottom of excavation	Elevation: 		ft

(  Level	(  Free of rock or debris

e.	Bedding material						( NA

(  Description:					      	Depth: 			in.

(  Free of clods, large rocks, frozen matter and debris

(  If washed rock bedding, migration of fines has been managed

(  Compacted 						( NA	( Yes  	( No

f. 	Tank oriented correctly 			(

g.	 Structural integrity of tank verified			(

h. 	Tank installed level 		( Yes  	( No

3. 	Insulation		( NA

(  Tank		Type:

(  Access riser	Type:

(  Lid 		Type:

4.	Floatation (buoyancy) prevention

a.	Buoyancy calculation provided on design                		( Yes  	( No

b.	Anti-floatation implemented:	 	( NA	( Yes 		( No

( Tank collar

( Dead man

( Other:

5. 	Backfill

a. 	Backfill material:

(  If washed rock backfill, migration of fines has been managed

b. 	Compacted						( NA	( Yes  	( No

c.    Free of clods, large rocks, frozen matter and debris  		( Yes  	( No

6.	Piping

a.    Piping in appropriate sequence (inlet/outlet) 		( Yes  	( No

b. 	Pipe specifications (material and nominal diameter)

Inlet:

Outlet/Supply line:		( NA (Holding tank)

Return line:		( NA

Electrical conduit:		( NA

c.	Joints in excavated area			( Yes  	( No

d.	Pipes appropriately sleeved in excavated area	( NA	( Yes 	( No

Type of sleeve:

e.	Piping sealed (including electrical conduit)                	( Yes  	( No

Type of sealant:

Inlet:

Outlet/Supply line:

Return line:		( NA

Electrical conduit:		( NA

f.	Recirculation device			( NA	( Yes 	( No

Type of device:

7.	Baffles/compartments/vaults

a.	Inlet baffle

i. Type

(  NA	(  Sanitary tee	(  Plate	( Wall

ii. Installation by

(  Manufacturer    		(  Contractor

b.	Outlet baffle

i. Type

(  NA	(  Pipe tee or sanitary tee	(  Plate	  (  Effluent screen

Model:

Manufacturer:

ii. Installation by

(  Manufacturer		(  Contractor

c.	Compartment baffles:

i. Type

(  NA	(  Tee baffle	(  Slot	(  Center hole

ii. Installation by:

(   Manufacturer			(   Contractor

iii.	(   Verify air passage

d.	Solids management 					( NA

Type:

( Shield			( Vault with basket	( Vault with screen

Manufacturer:

Model #:

8.	Tank access and venting

a.	Access location and size (diameter and depth):

( Inlet:

( Outlet:

( Center:

b.	Access risers and associated lids 		( Yes  	( No

Riser manufacturer:

Model #:

Lid manufacturer:

Model #:

Traffic rated (AASHTO H-20/HS-20)		( Yes  	( No

Interior access:  		(  Second lid       (  Grate   	(  Netting 	(  NA

c.	Installation

( Cast in place

( Installed by tank manufacturer

( Installed on the site by the contractor

d.   	Sealant used in tank/riser connections		( NA	( Yes 	( No

Type of sealant:

e. 	 Venting

( Through plumbing stack

( Tank vent (describe):

( Proprietary filter:

Filter manufacturer:

Model #:

9. 	Tank watertightness testing:

( Not required

( Manufacturer-tested

( Field tested

Method:				( Water	( Vacuum

Results:				( Pass	( Fail

10.	Septic tank/grease trap/holding tank alarm(s)  				( NA

a.	High-water alarm(s) present            		( Yes  	( No

(  Mechanical non-powered alarm

(  Electrical powered alarm

Manufacturer:

Model #:

b.	Remote telemetry				( Yes  	( No

Manufacturer:

Model #:

11.  Final cover

a.	Material:

b.	Sloped to allow for settling and shedding water		( Yes  	( No

12.  Site stabilization

(  Erosion control measures in place	(  Topsoil dressed

(  Seeded				(  Mulched

# Text boxes

Comments: (Indicate if photographs were taken)

Comments: (Indicate if photographs were taken)

Comments: (Indicate if photographs were taken)