Form 9.2. Startup checklist: Timed and demand dosed pumps and siphons.

Client name:			 Reference #:

Permit(s) #:

Completed by:		 Time:			 Date:

System type:    ( Pump   ( Siphon

1.	Controls                                    					( NA

a.	Type:          ( Piggyback              ( Control panel

Manufacturer:

Model:

b.	Installation check

( Enclosure watertight

( Enclosure rated NEMA 4X

( Alarm test switch working properly   					( NA

( Control switch (HAND-OFF-AUTO) operable 				( NA

( Control switch (HAND-OFF-AUTO) set at:

( Auto

( Hand/Manual	Why:

( Off 	Why:

( Timer operable   							( NA

Timer setting:  		On Mode setting 						min.

Off Mode setting 					min. or hr.

( Elapsed time meter (ETM) operable  					( NA

Meter reading:

( Cycle counter operable							( NA

Counter reading:

( Telemetry operable   							( NA

2. 	Pump

a.  	Pump manufacturer:

Model:

b.	Type of pump:   	( Multi-stage  	( Single-stage

( Sewage  	( Effluent	( Grinder

c.	Pump specifications:

i.	Design flow rate:										 gpm

ii.	Design pressure (tdh):										ft

iii.	Horsepower: 							hp

d.    Pump operable                      				( Yes  	( No

e.	Pump intake elevated:   Height	                         	  in.		( Yes  	( No

f.	Pump installed under access					( Yes  	( No

g.   	Pump removal

( Pull chain or rope installed  	( Pump rails installed

( Other:

h.	Pump vault flow rating: 						 gpm	( NA

i.    	Electrical considerations (PERFORMED BY QUALIFIED INDIVIDUALS ONLY)

(	Power supply available

(	Amps measured: 						 amps

(	Voltage measured:						 volts

(	Electrical service

( 	Single-phase 120V	( Single-phase 240V

( 	3-phase 240/120V	( 3-phase 208/120V

(	Power supply appropriate for unit

(	Distance from control panel to disconnect:					 ft

3.    Siphon										( NA

a.  	Siphon operable   						( Yes  	( No

b.  	Siphon installed under access  					( Yes  	( No

c.  	Siphon removable						( Yes  	( No

d.  	Siphon cycle counter operable				( NA 	( Yes  	( No

4.   Pump discharge assembly components installed

(	Assembly reachable from surface

- Quick disconnect operable

- Isolation valve operable	    						( NA

- Anti-siphon/air release device operable                 			( NA

- Backflow prevention (check valve) 	operable        				( NA

(	Air release located below check valve operable    				( NA

( 	Drainback device operable                                 				( NA

- Inline filter operable    	              						( NA

- Pressure gauge /port operable     	              				( NA

- Sampling port operable    	              						( NA

5.	Water level sensors

a. 	Type of water level sensor:  	( Floats        		( Pressure transducers

( Ohm probe   	( Other:

b.    Sensor attachment

(   	Tethered to float tree

(    	Weighted tether from riser

(    	Attached to riser

c.  	Float tree removable  					( NA 	( Yes  	( No

d.  	Pump floats/sensors settings

| Sensor number* | Function | Operational | Set at** | Secured |
| --- | --- | --- | --- | --- |
|  |  |  | Inches | Datum |  |
| 1 |  | ( Yes ( No |  |  | ( Yes ( No |
| 2 |  | ( Yes ( No |  |  | ( Yes ( No |
| 3 |  | ( Yes ( No |  |  | ( Yes ( No |
| 4 |  | ( Yes ( No |  |  | ( Yes ( No |
| 5 |  | ( Yes ( No |  |  | ( Yes ( No |

*Designate starting from bottom of tank.

**Measurements are taken from a fixed point (“Datum”) near the surface or bottom of float in inches.

e.  	Alarm float/sensor operates audible alarm 	( NA 	( Yes  	( No

f.  	Alarm float/sensor operates visible alarm 	( NA 	( Yes  	( No

g.	Pump submerged at OFF elevation	( NA 	( Yes  	( No

6.	Performance verification

a.		Design parameters (from permit or plans):

Dosing regime:

( Demand dosing

( Timed dosing

Design volume (DeV):

Design Timer settings:  						(  NA

On setting					 min.

Off setting	       				 min. or hr.

Design PDR:								 gal/min.

Design operating pressure:          				 feet or psi

b.		Dose volume (DV) verification

i.	Calculate design drawdown (inches)

[DeV (gal.)] ÷ 	  gal/in.  = 	Design drawdown (in.)

ii.    Verify DV during a dosing event

Method to activate pump:        ( Water added/pump in AUTO              ( Lifted float

Pump run time during dosing event: 		 min.

Measured drawdown during dosing event:

Pump off (in.)  –  	 Pump on (in.)  =  			 Measured drawdown (in.)

Calculate measured DV

Measured drawdown (in.) x 		  gal/in. =   	                Measured DV (gal.)

Subtract drainback volume if appropriate:

Measured DV (gal.) - 		 Drainback volume (gal.) =  		 Net DV (gal.)

c.  	Timer setting verification   							(  NA

i.   	Timer operation verified   							(

ii.  	Method of verification:

d.	Pump delivery rate (PDR) verification

i.    	Measured DV (from Item 6a ii): 	 gal.

ii.   	Verified pump run time 	 min.

iii.   Measured PDR: 		 gal. pumped ÷ 		 min.  = 		 gal/min.

e.    System pressure verification

i.    	Measured operating pressure: 		feet or psi

ii.   	Measurement location:

ETM: elapsed time meter

DeV: design dose volume

DV:  dose volume

gpi: gallons per inch

gpm:  gallons per minute

HAND-OFF-AUTO:  Hand-Off-Auto Switch

PDR: pump delivery rate

psi:  pounds per square inch

# Text boxes

Comments:

Comments:

Comments: