Form 7-2 Operational Checklist:  Aerobic treatment unit (ATU)

Service provided on:   Date:                Time:                        		Reference #:

Service provided by:   Company: 				     	  	Employee:

Date of last service: 		 		By:  ( You   ( Other:

Date of last inspection: _______________________________

1.	Type of ATU:

( Suspended-growth   ( Attached-growth    	( Sequencing batch reactor

( Combination attached/suspended-growth

( Rotating biological contactor	 		( Other:

a.	Manufacturer:	    Model #:

2.	Conditions at the ATU

a.	Evaluate presence of odor within 10 ft of perimeter of system:

( None     ( Mild     ( Strong      ( Chemical     ( Sour

b.	Source of odor, if present: ________________________________

c.    Was foam/residue observed outside the unit.	Yes	No

3.	ATU access

a.	Located at grade.	Yes	No

b.	If ‘No’, how deep is tank buried.

c.	Risers on tank.	Yes	No

d.	Evidence of infiltration in the risers.	Yes	No

e.	Lids securely fastened.	Yes	No

f.	Lids in operable condition.	Yes	No

4.	Venting/Air supply

a.	Air supply method:

( Aspirator ( Aerator ( Compressor ( Blower ( Free air (go to 4.g)

b.	Operation:  ( Continuous	( Timed (On: 	min, Off:  	 min)

c.	Air supply unit operating properly.	Yes	No

d.	Pressure at air supply unit:			psi

e.	Air flow at air supply unit:			cfm

f.	Air filter/screen:   ( Cleaned	( Replaced

g.	Venting appears operable.	                             Yes ____No____

5.	Aeration chamber

a.	Mixing in aeration chamber.	Yes	No

b.	DO in aeration chamber:		 	mg/L

c.	pH in aeration chamber:

d.	Temperature in aeration chamber:

e.	Settlability test:

Settled 	%, Floating 	%  in 	 min

f.	Biomass color in the aeration chamber:

(Brown	(	Black

g.	Sludge pumping recommended.	Yes	No

6.	Additional tasks for attached-growth: media evaluation

a.	Plugging.	Yes	No

b.	Floating.	Yes	No

c.	Media washed.  		                             Yes____No_____

If washed, indicate method used:           ( Air      ( Water

d.	Media replaced. 	Yes	No

7.	Clarification chamber

a.	Scum layer.	Yes	No

If yes, thickness:			in

b.	Clear zone depth below outlet:   			in

c.	Effluent screen/tertiary filter cleaned.	N.A.___Yes	 No

Reference #:

d.	DO in clarifier:		 	mg/L

e.	pH in clarifier:

f.	Temperature in clarifier:

g.	Effluent odor after passing through unit:

(	None	(	Mild	(	Strong									h.	Effluent color after passing through unit:

(	Clear	(	Brown	(	Black

i.	Effluent turbidity:				NTU

8.	Sludge return operating:                                          ( Passive    ( Active

a.	If active, pump was checked manually. 	N.A.___	Yes	No

b.	If active, pump operating properly.	N.A.___	Yes	No

9.	 Control Panel:     				N.A.__________________

a.	Controls operating properly. 			Yes	No

b.	Is enclosure watertight.			Yes	No

c.	Alarm test switch operating properly.		Yes	No

d.	At time of inspection, control switch was set to: 	N.A.___________

“Hand/Manual”__

“Auto”_________

e.	If auto, setting:    Time On:_______ (min) Time Off:________ (min)

10.	Alarm(s): 			N.A.___________

a.	Types:	( Air pressure	( High water     ( Remote

b.	Alarms operating.			Yes	No

c.	Alarm readings:

|  | Reading (present) | Reading (last) | Difference | N.A. |
| --- | --- | --- | --- | --- |
| i. | ETM |  |  | hours |  |
| ii. | Alarm Counter |  |  | Events (NC) |  |

Elapsed time in alarm status:  _____(PTR) - _____(LTR)   = ______Time (hours)

Number of alarm events:    	(PACR) - _____(LACR) = ______Events (number)

d.	Battery backup charged.		N.A.___Yes	No

e.	Telemetry operable.		N.A.___	Yes	No

11.	Manufacturer’s required maintenance performed.	Yes	No

(If ‘Yes’, attach Manufacturers Inspection form to this report, if supplied)

12.	Lab samples collected for monitoring.	Yes	No

Types of analysis:

ETM: elapsed time meter

LACR: last alarm counter reading

LTR: last time reading

NC: number of cycles

PACR: present alarm counter reading

PTR: present time reading

# Text boxes

8.  ( Acceptable

( Unacceptable

9.  ( Acceptable

( Unacceptable

10.  ( Acceptable

( Unacceptable

2.  ( Acceptable

( Unacceptable

3.  ( Acceptable

( Unacceptable

4.  ( Acceptable

( Unacceptable

5.  ( Acceptable

( Unacceptable

6.  ( Acceptable

( Unacceptable

7.  ( Acceptable

( Unacceptable

NOTES